## Slide 1: Hardware based Intrusion Detection System
2ND Progress Report

## Slide 2: Steps Completed
Installing Minibian OS
Setting up Pi
Adding User
Installing WiFi and Bluetooth Drivers
Installing the DHCP server

## Slide 3: Steps Completed (cont..)
Installing HostAPD
Configure the ISC-DHCP-Server
Configuring HostAPD
instantiating Router
NAT Configuration

## Slide 4: Installing OS

## Slide 5: Setting Up Pi
Updating Debian Packages :
  Sudo apt-get update
  Sudo apt-get upgrade
Upgrading Firmware :
  Sudo apt-get rpi-config
  Sudo rpi-update

## Slide 6: Adding User and installing drivers
Add user commands:
  Useradd username(pi)
  Password(pids)
sudo apt-get install firmware-brcm80211 pi-bluetooth wpasupplicant
Sudo apt-get install hostapd

## Slide 7: Installing and configuring DHCP server
sudo apt-get install isc-dhcp-server
Configuring:
  sudo nano /etc/dhcp/dhcpd.conf
    commenting:
      option domain-name "example.org";
      option domain-name-servers ns1.example.org, ns2.example.org;
    un-commenting:
      #authoritative;

## Slide 8: Cont..
  adding:
    subnet 192.168.10.0 netmask 255.255.255.0 {
    range 192.168.10.10 192.168.10.20;
    option broadcast-address 192.168.10.255;
    option routers 192.168.10.1;
    default-lease-time 600;
    max-lease-time 7200;
    option domain-name "local-network";
    option domain-name-servers 8.8.8.8, 8.8.4.4;
    }
  sudo nano /etc/default/isc-dhcp-server
    specifying wireless interface
      INTERFACES="wlan0"
  Giving Static IP Address to Pi:
  sudo ifdown wlan0
  sudo nano /etc/network/interfaces

## Slide 9: Configuring HostAPD
AP name and Pass:
  sudo nano /etc/hostapd/hostapd.conf
    adding:
      “ssid=wifi”
      “wpa_passphrase=YourPassPhrase”
  Enabling NAT:
    sudo nano /etc/sysctl.conf
      adding:
        net.ipv4.ip_forward=1
        sudo sh -c "echo 1 > /proc/sys/net/ipv4/ip_forward"

## Slide 10: NAT configuration
translation between the ethernet and wireless card
  sudo iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
  sudo iptables -A FORWARD -i eth0 -o wlan0 -m state --state RELATED,ESTABLISHED -j ACCEPT
  sudo iptables -A FORWARD -i wlan0 -o eth0 -j ACCEPT

## Slide 11: NAT Configuration (cont..)
backing up NAT Config
  sudo sh -c "iptables-save > /etc/iptables.ipv4.nat"
adding NAT Config to interface file
  sudo nano /etc/network/interfaces
  adding:
    up iptables-restore < /etc/iptables.ipv4.nat

## Slide 12: Instantiating router
Starting router
  sudo service isc-dhcp-server start
  sudo service hostapd start
Run At Startup
  sudo update-rc.d hostapd enable
  sudo update-rc.d isc-dhcp-server enable